Calculation of Dimesions for Solar Thermal System

Apricus Solar Heater ETC-30: 2.84 m² (dimesnions: 2005x2196x136 mm)

Annual Solar Radiation: 5.44 kWh/m2/day (according to: pvwatts.nrel.gov/)

Efficency: 50%

5.44 * 2.85 * 0.5 = 7.7248 kWh per ETC-30

Energy Needs (http://processheatingservices.com/water-heating-time-calculator/):

Heating 200L of 20C Water to 60C (delta 40): 9.37866 kWH

2 ETC-30, or other collectors of equivalent surface are sufficient to heat water in one container.